## Slide 1: Application of Q Estimation at Basin Scales
Sam Poulter

## Slide 2: Project Outline:
Aim:
  To produce a regional view of effective seismic attenuation as derived from stacked traces & volumes data, by applying the Spectral Ratio method to stacked seismic sections around the North Sea region.
Objectives:
  1.Develop automated Spectral ratio code
  2. Validate code by testing and applying it to synthetic wavelets.
  3. Adapt code into AWS workspace and run on all UK regional lines
  4. Assess any correlations of regional Q values through clustering
  5. Assess if these correlations could be useful in predicting data quality and resolution

## Slide 3: What Is Q?
Attenuation is the loss of amplitude during the propagation of a seismic wave through an attenuating material and quantified by the seismic quality factor Q
Attenuation causes a loss of vertical resolution and results in a lower amplitude and lowers the dominant frequency of traveling wavelets .
Also has a phase effect, as low frequencies must travel slower than high frequencies

## Slide 4: Why are we interested
Corrections during processing seismic data
- Amplitude recovery
- AVO corrections
-Compensate for loss of resolution
Used as a indicator for reservoir properties
  -Gas saturation
  -Fracture Azimuth
  -Monitor injection processes

## Slide 5: Causes of Intrinsic attenuation
Rock Frame Causes:
1. Friction at grain boundary
2. Compression of fractures and micro cracks
Fluid Saturation Effects:
1. Fluid flow in and out of fractures
2.Bubble Compression
3. Squirt Flow
After Jonhston 1979

## Slide 6: Methods of Measuring: Spectral Ratio
Frequency Independent Mechanisms e.g. Geometric Spreading G, Reflectivity R

## Slide 7: Synthetic Attenuated Trace
No attenuation to see the effect of windowing function and general Fourier artefacts
Hanning filter – Spectral properties
Input wavelet – 100Hz ricker
Spiked Reflectivity
Final Trace

## Slide 8: No AttenSpectral Ratios
Near zero gradient gives infinite Q
Small gradient affects due transform artefacts and imprint of window spectrum on data
Spectra of all possible window combinations

## Slide 9: Noise less synthetic
Trace with Q = 150
Spiked Reflectivity
Using Kjartansson's 1979 constant Q model

## Slide 10: Spectral Ratios
Ratio of two windows over non- events
Ratio of two windows over events
Ratio of windows over edge of event
Spectra of all possible window combinations

## Slide 11: Noisy Synthetic
Band limited noise rather than random white noise
Noisy Attenuated Trace
Pseudo Random Reflection Series – Still with 6 spikes
Band limited noise rather than random white noise

## Slide 12: Spectral Ratios
Noise in the synthetic results in spikier spectral ratios
Spectra of all possible window combinations
Ratio of two windows over events
Ratio of two windows over two non events

## Slide 13: QC- Finding optimal window pairing
Error calculation:
Tartan Triangle for 1/Q
Tartan Triangle for 1/Q error
Tartan Triangle for 1/Q weighted by the error in Q

## Slide 14: Methods of Automating the QC
Hilbert Transform
3. RMS of trace window
1. Take product of analytic signal in each investigation window
2. Set cut off above noise level, conduct spectral ratio on only data above level

## Slide 15: Future Work
Optimise bandwidth for line fitting
Apply to single trace of real data
Apply at scale

## Slide 16: Thesis Overview
1. Introduction
          Motivation for project
          Aims and objectives
2. Methodology and Background
          Overview of Q
          Uses of Q
          Q estimation
3. Results
          Synthetic trace results
          Regional Scale results
5. Conclusions
4. Interpretation and Discussion
          Q clustering
          Assess any correlations of regional Q values